Revised Design Goals

# Specification

( 2 Person short take-off and landing general aviation aircraft

( Ability to fit on a trailer or roof mounted on a car for transportation

( Simple lightweight design using modern propulsion systems

( Failsafe modes to ensure pilot safety – particularly important for landing and take-off

( Higher performance than typical microlight aircraft

( Meet certification requirements where applicable

# Performance

( Take-off and landing ground run should not exceed 46 m (150 ft)

( Take-off and landing distance over a 16 m (50 ft) obstacle should not exceed 152 m (500 ft)

( Stall speed should not exceed 37 kts

( Sea level max cruising speed should be in excess of 140 kts

( Range at typical cruising speed should be in excess of 400 nm

( Endurance should be greater than 2 hours

( Sea level maximum rate of climb should be greater than 1000 ft/min