My favorite airplane

V-22 Osprey

– A tiltrotor aircraft

AOE4984

Configuration Aerodynamics

Instructor: Dr. Mason

By: Wang Hongwei

V-22 Osprey – A tiltrotor aircraft

Is it a helicopter or an airplane?

A tiltrotor aircraft.

Helicopter + Airplane = Heliplane.

## What it is:

- When the engines are vertical, the tiltrotor aircraft operates like a helicopter. The rotors provide lift and control.

- As the engines are tilted downward, the tiltrotor aircraft accelerates. The wings generate lift as speed increases. Control is achieved via the rotors and conventional aerodynamic surfaces.

- when the engines are horizontal, the tiltrotor operates as a conventional turboprop airplane. Lift is provided by the wings and control is provided by conventional airplane control surfaces.

1. History:

( The Bell XV-3 in the 1950s and 60s demonstrated concept feasibility.

( The Bell XV-15 in the 1970s demonstrated technology maturity.

( In 1982, Bell and Boeing teamed to develop the V-22 Osprey, V-22 first

fly in 1989.

( The Bell-Boeing V-22 in the 1980s and 90s proved tiltrotor capabilities,

mission suitability, producibility and affordability.

( The U.S. Government and Industry have invested 40 years and $5 billion

developing tiltrotor technology.

TILTROTORS - A UNIQUE TECHNOLOGY MADE ONLY IN THE USA.

2. Why tiltrotor?

- Better than a helicopter

( High speed

( High altitude

( More quiet

( Less vibration ( Better reliability ( Lowering costs.

- Better than an airplane

( Vertical takeoff and landing ( More flexible

( Engines at tip ( Higher yaw inertial

3. Specifications:

#### Aerodynamic Characteristics:

- Span: 41ft 1.75in

- Chord: 8ft 0.90in

- Tape Ratio: 1.0

- Sweep angle: -7( (Fore Sweep)

- Aspect Ratio: 5.1

- H Tail

#### Dimensions

- Length, fuselage - 57.33 ft (17.48 m)

- width, rotors turning - 83.83 ft (25.55 m)

- Height, nacelles fully vertical - 22.08 ft (6.73 m)

#### Weights

- Empty 33,140 lb (15,032 kg)

- Takeoff, vertical, maximum 47,500 lb (21,546 kg)

#### Performance

- Maximum speed at sea level - 275 kt (510 km/hr)

- Vertical rate of climb at sea level - 1,090 ft/min (332 m/min )

- Maximum rate of climb at sea level - 2,320 ft/min (707 m/min)

- Service ceiling - 26,000 ft (7,925 m)

#### Engines

- Manufacturer - Allison Gas Turbine Division

- Model - Two T406-AD-400

- Maximum and Intermediate - 6,150 shp (4,586 kw)

#### Rotor System

- Blades per hub - three

- Construction - graphite/fiberglass

- Tip speed - 661.9 fps (201.75 mps)

- Diameter - 38 ft (11.58 m)

4. V-22 design

Bell-Boeing Team Work Split

V-22 Program Schedule

Wind Tunnel Test

Flight Test:

| Shipboard Compatibility | External Loads | Confined Area Landings |
| --- | --- | --- |

Multimission use by all military services

|  | Combat Assault |  | Long-Range Special Operations |
| --- | --- | --- | --- |
|  | Combat Search & Rescue |  | Medical Evacuation |
|  | Assault Support |  | Special warfare |
|  | Fleet Logistics Support |  |  |

5. Future Tiltrotor Development

# Passenger plane

- An airplane that doesn't require a runway

- Speed, range and altitude of turboprops

- All-weather operations

- Multi-use aircraft

# Transportation plane

- Fast, convenient, cost-competitive

- Point-to-point air service

- Increased airport passenger throughput

- Simplified access to congested urban areas

- A new link in intermodal transportation

Reference:

http://www.v-22.com/

http://www.boeing.com/rotorcraft/military/v22/

http://www.navair.navy.mil/v22/index.htm

http://www.theaviationzone.com/facts/v22.htm

http://www.airforce-technology.com/projects/osprey/index.html

http://www.bellhelicopter.textron.com/products/tiltRotor/v22/index.html

http://www.ainonline.com/haiday2_v22.htm

http://www.boeing.com/rotorcraft/military/v22/v22news.htm